The involved nodes
eNodeB
nodeB
UE
X
S-GW
P-GW
GGSN
SGSN
RNC
MME
Assumption: the LTE and the UMTS networks belong to the same operator
→ P-GW = GGSN (they are the same device)
LTE
UMTS

---
The involved nodes

---
Preparation phase
Uplink and Downlink User Plane PDUs
 GTP tunnels
Bearers
Before the handover the UE is connected and user
plane PDUs (user data) are being transferred through
the showed path

---
Preparation phase
1) Handover initiation
2) Handover required
(S1 interface)
Message parameters:
S1AP Cause, Target RNC Identifier, CSG ID,
 CSG access mode, Source to Target Transparent Container

---
Preparation phase
1) Handover initiation
Message parameters:
IMSI, CSG ID, CSG Membership Indication, MM Context,
PDN Connections, Source to Target Transparent Container,
 RAN Cause, ISR Supported
2) Handover required
(S1 interface)
3) Forward relocation request
(S3 interface)

---
Preparation phase
1) Handover initiation
Message parameters:
4) UE Identifier, Cause, Encryption information RAB to be setup list,
CSG ID, CSG Membership Indication, Source RNC to Target RNC Transparent
Container
4a) Target RNC to Source RNC Transparent Container, RABs setup list,
RABs failed to setup list.
2) Handover required
(S1 interface)
3) Forward relocation request
(S3 interface)
4) Relocation request
(Iu-PS interface)
4a) Relocation request ACK

---
Preparation phase
1) Handover initiation
Message parameters:
5) Cause, SGSN Tunnel Endpoint Identifier for Control Plane,
SGSN Address for Control Plane, Target to Source Transparent Container,
Address(es) and TEID(s) for User Traffic Data Forwarding
2) Handover required
(S1 interface)
3) Forward relocation request
(S3 interface)
4) Relocation request
(Iu-PS interface)
4a) Relocation request ACK
5) Forward relocation response
(S3 interface)

---
Preparation phase
1) Handover initiation
Message parameters:
6) Address(es) and TEID(s) for Data Forwarding (received in step 5)),
EPS Bearer ID(s)
6a) Cause, Serving GW Address(es) and TEID(s) for Data Forwarding
2) Handover required
(S1 interface)
3) Forward relocation request
(S3 interface)
4) Relocation request
(Iu-PS interface)
4a) Relocation request ACK
5) Forward relocation response
(S3 interface)
  6) Create Indirect Data Forwarding Tunnel Request
(S11 interface)
  6a) Create Indirect Data Forwarding Tunnel Response

---
Preparation phase
1) Handover initiation
2) Handover required
(S1 interface)
3) Forward relocation request
(S3 interface)
4) Relocation request
(Iu-PS interface)
4a) Relocation request ACK
5) Forward relocation response
(S3 interface)
  6) Create Indirect Data Forwarding Tunnel Request
(S11 interface)
  6a) Create Indirect Data Forwarding Tunnel Response

---
Execution phase
1) Handover command
(s1 interface)
Message parameters:
Target to Source Transparent Container, E-RABs to Release List,
 Bearers Subject to Data Forwarding List

---
Message sent through the DCCH downling logical channel
DCCH → DL-SCH → PDSCH
1) Handover command
(s1 interface)
2) E-UTRAN HO command
(uu interface)

---
3) UTRAN lu Access procedures
3a) Handover to UTRAN complete
(uu – Iub interfaces)
Sending of user uplink data is now possible
1) Handover command
(s1 interface)
2) E-UTRAN HO command
(uu interface)

---
3) UTRAN lu Access procedures
If direct forwarding applies
If indirect forwarding applies
1) Handover command
(s1 interface)
2) E-UTRAN HO command
(uu interface)
3a) Handover to UTRAN complete
(uu – Iub interfaces)
Downlink user data
(Passing through SGSN if direct tunnel is not used)
Uplink user data

---
If direct forwarding applies
If indirect forwarding applies
(Passing through SGSN if direct tunnel is not used)
4) Relocation complete
(Iu-ps interface)

---
If direct forwarding applies
If indirect forwarding applies
(Passing through SGSN if direct tunnel is not used)
4) Relocation complete
(Iu-ps interface)
  5) Forward Relocation Complete notification
(s3 interface)
5a) Forward Relocation Complete ACK

---
If direct forwarding applies
If indirect forwarding applies
Message parameters:
SGSN Tunnel Endpoint Identifier for Control Plane, NSAPI(s),
SGSN Address for Control Plane, SGSN Address(es) and TEID(s) for
User Traffic for the accepted EPS bearers (if Direct Tunnel is not used)
or RNC Address(es) and TEID(s) for User Traffic for the accepted EPS bearers
(if Direct Tunnel is used), ISR Activated.
(Passing through SGSN if direct tunnel is not used)
4) Relocation complete
(Iu-ps interface)
  5) Forward Relocation Complete notification
(s3 interface)
5a) Forward Relocation Complete ACK
6) Modify Bearer Request
(s4 interface)

---
If direct forwarding applies
If indirect forwarding applies
Message parameters:
Cause, Serving GW Tunnel Endpoint Identifier for Control Plane,
Serving GW Address for Control Plane, Protocol Configuration Options, MS Info
Change Reporting Action
(Passing through SGSN if direct tunnel is not used)
4) Relocation complete
(Iu-ps interface)
  5) Forward Relocation Complete notification
(s3 interface)
5a) Forward Relocation Complete ACK
6) Modify Bearer Request
(s4 interface)
7) Modify Bearer Response

---
If direct forwarding applies
If indirect forwarding applies
The new user data path
(passing through SGSN only if direct tunnel is not used)
(Passing through SGSN if direct tunnel is not used)
4) Relocation complete
(Iu-ps interface)
  5) Forward Relocation Complete notification
(s3 interface)
5a) Forward Relocation Complete ACK
6) Modify Bearer Request
(s4 interface)
7) Modify Bearer Response

---
(passing through SGSN only if direct tunnel is not used)
8) Routing area update procedure
9) Delete Indirect Data Forwarding Tunnel Request

---
Handover Reject
1) Handover initiation
2) Handover required
(S1 interface)
3) Forward relocation request
(S3 interface)
4) Relocation request
(Iu-PS interface)
4a) Relocation failure
5) Forward relocation response
(S3 interface)
6) Handover preparation failure