Preparation
eNodeB
Target
RNC
UE
 SGSN
Source
S-GW
PDN
GW
MME
1) Handover initiation

---
Message parameters:
S1AP Cause, Target RNC Identifier, CSG ID,
 CSG access mode, Source to Target Transparent Container
2) Handover required
(S1 interface)

---
IMSI, Target Identification, CSG ID, CSG Membership Indication, MM Context,
PDN Connections, MME Tunnel Endpoint Identifier for Control Plane,
MME Address for Control plane, Source to Target Transparent Container,
 RAN Cause, MS Info Change Reporting Action (if available), CSG Information
Reporting Action (if available), UE Time Zone, ISR Supported, Serving Network
3) Forward relocation request
(S3 interface)

---
4): IMSI, SGSN Tunnel Endpoint Identifier for Control Plane,
SGSN Address for Control plane, PDN GW address(es) for user plane,
PDN GW UL TEID(s) for user plane, PDN GW address(es) for control plane,
and PDN GW TEID(s) for control plane, the Protocol Type over S5/S8,
Serving Network
4a) Serving GW address(es) for user plane, Serving GW UL TEID(s) for user plane,
Serving GW Address for control plane, Serving GW TEID for control plane
4) Create session request
(S4 interface)
4a) Create session response

---
5) UE Identifier, Cause, CN Domain Indicator, Integrity protection information,
Encryption information RAB to be setup list, CSG ID, CSG Membership Indication,
Source RNC to Target RNC Transparent Container,
Service Handover related information
5a) Target RNC to Source RNC Transparent Container, RABs setup list,
RABs failed to setup list.
5) Relocation request
(Iu-PS interface)
5a) Relocation request ACK

---
6) Target RNC Address and TEID(s) for DL data forwarding
or
SGSN Address and TEID(s) for DL data forwarding
6a) Cause, Serving GW Address(es) and Serving GW DL TEID(s) for data forwarding
        6) Create Indirect Data Forwarding Tunnel session request
        6a) Create Indirect Data Forwarding Tunnel session response

---
7) Cause, SGSN Tunnel Endpoint Identifier for Control Plane,
SGSN Address for Control Plane, Target to Source Transparent Container,
RAB SetupInformation, Additional RAB Setup Information,
Address(es) and TEID(s) for User Traffic Data Forwarding,
Serving GW change indication
        6) Create Indirect Data Forwarding Tunnel session request
        6a) Create Indirect Data Forwarding Tunnel session response
7) Forward relocation response

---
8) Address(es) and TEID(s) for Data Forwarding (received in step 7)),
EPS Bearer ID(s)
8a) Cause, Serving GW Address(es) and TEID(s) for Data Forwarding
        6) Create Indirect Data Forwarding Tunnel session request
        6a) Create Indirect Data Forwarding Tunnel session response
7) Forward relocation response
  8) Create Indirect Data Forwarding Tunnel Request
(S11 interface)
  8a) Create Indirect Data Forwarding Tunnel Response